## Slide 1: Cummins Westport Overview
Gordon Exel
Vice President and General Manager Americas
September 2011

## Slide 2: Cummins Westport Inc. (CWI) is a Joint Venture of Westport & Cummins
Cummins Inc.
“CWI”
Cummins Westport Inc.
50/50
Cummins Inc.
Westport Innovations Inc.
Established in 2001

## Slide 3: CWI: Fully integrated within Cummins. We are Cummins’ automotive natural gas engine company
Product
Engineering
Cummins Tech Center
Cummins VPI Process
Cummins Account
Teams & Distributors
Manufacturing
Warranty
Cummins Plants
Parts
& Service
Cummins Distributors
Sales
Cummins Warranty

## Slide 4: Technology What is the Same?
Major Engine Components
  Block, crankshaft, main bearing, piston rods, EGR
  Over 80% parts commonality
500 hour Maintenance Interval
Parts and Service
  Global Cummins Distributor Network
320, 300, 280, 260 and 250 HP ratings
Compatible with Cummins Diagnostic tools
  Insite
  Quickserve online
Manufactured in Cummins Engine Plant, North Carolina

## Slide 5: Technology What is Different?
Cylinder head
  2 valve vs. 4 valve (diesel)
Ignition
  Spark Ignition (SI) vs. Compression (diesel)
Fuel System
  Intake manifold vs. Common rail injection (diesel)
Aftertreatment
  3 way catalyst vs. Particulate Filter + Selective Catalytic Reduction (diesel)
Maintenance Cost
  Incremental cost of maintenance related to ignition and overhead valve adjustments adds up to $0.03 per mile ($0.02 per km) to ISL G
Fuel Cost
  Natural gas costs less than diesel
  Fuel cost per mile (KM) is lower.
Lubricating Oil
  Natural gas engines require a specific oil that meets Cummins specification CES 20074
Noise
  Natural gas engines are up to 10db quieter at idle
Compression Ratio
  ISL G is 12:1 compression
  Lower power density

## Slide 6: Estimated System Weight ~ 60 Gallons Fuel CNG – 1,000 lbs more LNG – 300 lbs more
System Weights | ISL9 Diesel | ISL G Natural Gas
Engine | 1,695 lbs | 1,625 lbs
Aftertreatment | 400 lbs | 100 lbs
Fuel Tanks |  | 
- Diesel (60 Gal) | 100 lbs (600 lbs Full) | 
- CNG (60 DGE) |  | 1,600 lbs (2,000 lbs Full)
- LNG (68 DGE) |  | 815 lbs (1,288 lbs Full)
Total Weight (Full) | 2,695 lbs | CNG - 3,725 lb LNG - 3.013 lb

## Slide 7: 2010 Engines Aftertreatment Comparison
Cummins TWC
Heated
Urea Tank
Urea Dosing Control Unit
ECM
SCR Catalyst
Particulate Filter

## Slide 8: Tough California Emissions Standards and Cummins Westport Engines
 | NMHC |  | NOx |  | CO |  | PM | 
 | FTP | EURO | FTP | EURO | FTP | EURO | FTP | EURO
STD | 0.14 | 0.14 | 0.2 | 0.2 | 15.5 | 15.5 | 0.01 | 0.01
CERT | 0.13 | 0.04 | 0.13 | 0.01 | 1.2 | 0.4 | 0.002 | 0.000
California Air Resources Board - Executive Order Shows Emissions Results
ISL G is under 2010 NOx and PM regulations
FTP: Federal Test Procedure [ transient and steady state ]
EURO: Euro III European Steady-State Cycle
STD: standard or emissions test cap
CERT: certification level
Further Reductions are Being Explored
  Sub Ambient
  “Zero” Emissions

## Slide 9: Internal Combustion Engines & Green House Gases (GHG) Biomethane Impact
Bio Fuel improves GHG impact
Biomethane: 75-200% reduction
Compressed Natural Gas - 22% GHG reduction
Source:http://www.nsca.org.uk/assets/biogas_ as_transport_fuel_june06.pdf
Bowerman Landfill
WM Altamont
1,811.7 g/km
1,353.7g/km
9.7 g/km
179.5 g/km
268.8g/km
Diesel
1,402.4 g/km
1,183.9 g/km
53.9 g/km
49.5 g/km
115 g/km
Natural Gas
Total
End user
Transportation and storage
Processing
Extraction
Notes: Note the impact that Biomethane has on the GHG’s.

## Slide 10: Our initial assessment indicates the current ISL G is compliant for all 2014 GHG standards except HHD Tractor Trailer.
The ISL G meets vocational standards (incl. Urban Bus) in current form.
To meet Tractor Trailer standards, the ISL G may need Closed Crankcase Ventilation (CCV) and changes to catalyst coating formulation.
Neither change would be significant. If required for Tractor Trailer, would likely standardize across all applications.
MHD = Medium Heavy Duty
HHD = Heavy Heavy Duty

## Slide 11: Top North America CNG Transit Fleets
300
BOSTON
400
WASHINGTON
600
PHOENIX
300
SACRAMENTO
400
SAN DIEGO
250
SAN BERNADINO
250
TACOMA
over 8,000 engines in service
Las Vegas, NV
Ocean Side, CA
Culver City, CA
Baton Rouge, LA
Santa Clara, CA
Salem, OR
Toronto, ON
LA, CA — Foothill
Montgomery County, MD
St. Louis, MO
LA, CA — DOT
San Antonio, TX
Medford, OR
Fort Worth, TX
Port Huron, MI
Atlanta, GA
Seattle, WA
Fresno, CA
Long Island, NY
Hamilton, ON
Santa Monica, CA
Vancouver, BC
Albuquerque, NM
Corpus Christi, TX
Cape Cod, MA
1500
L A
500
ORANGE COUNTY
150
NYCT

## Slide 12: www.cumminswestport.com